## Slide 1: Physics 1210/1310
Mechanics
&
Thermodynamics
Lecture 39~40 Thermodynamics

## Slide 2
Phase Diagrams
For a substance which expands on melting
For an ideal gas

## Slide 3
First and Second Law of
Thermodynamics
And Types of Thermodynamic Processes

## Slide 4
Thermodynamic systems
Isolated systems can exchange neither energy nor matter with the environment.
Closed systems exchange energy
but not matter with the environment.
Heat
Work
reservoir
Open systems can exchange
both matter and energy with
the environment.
Heat
Work
reservoir

## Slide 5
Quasi-static processes
Quasi-static processes: near equilibrium
States, initial state, final state, intermediate state: p, V & T
well defined
Sufficiently slow processes = any intermediate state can be considered as at thermal equilibrium.
Criterion: It makes sense to define a temperature (ie)
there is a statistical average
Examples of quasi-static processes:
- iso-thermal: T = constant
- iso-volumetric: V = constant
- iso-baric: P = constant
- adiabatic: Q = 0

## Slide 6
Work done equals area under curve in pV diagram
Expansion: work on piston positive, work on gas negative
Compression: work on piston negative, work on gas positive

## Slide 7
1st Law: The change of the total energy of a
thermodynamic system depends on change of
heat in system and work done.
More generally DE = DK + DUg +DU

## Slide 8
State functions
a. isovolumetric
b. isobaric
a. isobaric
b. isovolumetric
isothermal
the work done by a system depends on the initial and final states and
on the path  it is not a state function.
energy transfer by heat also depends on the initial, final, and intermediate states
 it is not a state function either.
a
b
c

## Slide 9
Kinds of Thermodynamic Processes:
Adiabatic – no heat transfer (by insulation or by very
fast process)
U2 – U1 = -W
Isochoric – constant volume process (no work done
on surroundings)
U2 – U1 = Q
Isobaric – constant pressure process
W = p (V2 – V1)
Isothermal – constant temperature process (heat may flow but very
slowly so that thermal equilibrium is not disturbed)
DU, Q , W not zero: any energy entering as heat must leave as work

## Slide 10
Ideal gas – iso-volumetric process
Isovolumetric process: V = constant
V
P
V1,2
1
2
Heat
reservoir
During an iso-volumetric process, heat enters
(leaves) the system and increases (decreases)
the internal energy.
(CV: heat capacity
at constant volume)

## Slide 11
Ideal gas - isobaric process
Isobaric process: P = constant
V
P
V1
1
2
V2
(CP: heat capacity
at constant pressure)
During an isobaric expansion process,
heat enters the system. Part of the heat is
used by the system to do work on the
environment; the rest of the heat is used
to increase the internal energy.
Heat
Work
reservoir

## Slide 12
Ideal gas - isothermal process
Isothermal process: T = constant
V
P
V1
1
2
V2
Expansion: heat enters the system
all of the heat is used by the system
to do work on the environment.
Compression:
energy enters the system by the work done
on the system,
all of the energy leaves the system at
the same time as the heat is removed.

## Slide 13
Ideal gas - adiabatic process
V
P
V1
1
2
V2
Adiabatic process: Q = 0
Ideal gas:
Adiabatic process:
f is degree of freedom

## Slide 14
V
P
V1
1
2
V2
Ideal gas - adiabatic process (contd)
let
, and divided by

## Slide 15
V
P
V1
1
2
V2
Ideal gas - adiabatic process (contd)
For monatomic gas,
For diatomic gas, g = 1+2/5 = 1.4
f =5 at normal T (threshold not met)
f=7 at very high T

## Slide 16
V
P
V1
1
2
V2
or
Ideal gas - adiabatic process (contd)

## Slide 17
V
P
V1
1
2
V2
Ideal gas - adiabatic process (contd)
During an adiabatic expansion process, the reduction of the internal energy is
used by the system to do work on the environment.
During an adiabatic compression process, the environment does work on the system and increases the internal energy.

## Slide 18
Summary
Quasi-static
process
Character
adiabatic
isothermal
T = constant
isovolumetric
isobaric
V = constant
P = constant

## Slide 19: Thermodynamic Engines
Cyclic processes: DU = 0 or Q = W
Efficiency:
How much W per Q taken:
e = W/Q_H = (Q_H – Q_C)/Q_H
= 1 - Q_C/Q_H

## Slide 20: Thermodynamic Engines: Refrigerators (and heat pumps)
How much Q per W applied:
K = Q_C/W = Q_C/(Q_H – Q_C)

## Slide 21
Carnot Cycle
The best-e cycle
2 reversible isothermal
and 2 reversible adiabatic
processes.

## Slide 22
4 stroke or Otto engine
intake stroke
compression stroke
ignition
power stroke
exhaust stroke
Bottom right Ta, bottom left Tb
Use T*Vg-1 = const. law
for the two adiabatic processes
For r=8, j = 1.4 e=56%

## Slide 23
Diesel Cycle
Typical rexp ~ 15, rcomp ~ 5

## Slide 24
Second Law of Thermodynamics
No system can undergo a process where heat
is absorbed and convert the heat into work
with the system ending in the state where it
began: No perpetuum mobile.
b/c heat cannot
flow from a colder to
a hotter body w/o
a cost (work).
iow e=100% is not
possible!
Reversible vs irreversible
processes.

## Slide 25
Second Law of Thermodynamics:
gives direction to processes
No system can undergo a process where heat
is absorbed and convert the heat into work
with the system ending in the state where it
began: No perpetuum mobile.

## Slide 26
There are many other useful state functions:
the thermodynamic potentials
Enthalpy H = U + PV
Free energy at const P, T
G = U + PV - TS
Free energy at const. T
F = U – TS
Entropy S
etc.
The first law revised (for a p-V-T system):
DU= TdS - pdV

## Slide 27
Entropy: macroscopic interpretation:
Cost of Order – reversible and irreversible processes
Total entropy change zero:
reversible
Use dQ = T dS in first law!
DU = TDS - pDV
What is this entropy?
No easy answer, dep. on the case

## Slide 28
Entropy: microscopic meaning
Total entropy change zero:
reversible
w no of possible states

## Slide 29
Loose ends: The 3rd Law of Thermodynamics
3rd Law: It is impossible to reach absolute zero.

## Slide 30
‘Fun’ mnemonic about thermodynamic laws:
1st Law ‘You can’t win, you can only break even’
2nd Law ‘You can break even only at absolute zero’
3rd Law ‘You cannot reach absolute zero’
Moral: one can neither win nor break even
The American Scientist , March 1964, page 40A
The laws of thermodynamics give ALL processes a direction,
even the one’s in mechanics, E&M, etc.