## Slide 1: Circuits I

## Slide 2: Moving charges: Electric Current
Path of moving charges: circuit
Transporting energy
Current
http://dananne.org/dart/randomwalk/web/randomwalk.html
Random walk does not mean ‘no progression’
Random motion fast: 106m/s
Drift speed slow: 10-4m/s
e- typically moves only few cm
Positive current direction:= direction flow + charge

## Slide 3
Work done by E on moving charges  heat
(average vibrational energy increased i.e. temperature)
Current through A:= dQ/dt
charge through A per unit time
Unit [A] ‘Ampere’
[A] = [C/s]
Concentration of charges n [m-3] , all move with vd, in dt moves vddt,
volume Avddt, number of particles in volume n Avddt
What is charge that flows out of volume?
dQ = q (n Avddt)  current dQ/dt = n qvdA
Current density [A/m2] J = I/A = nqvd
Current and current density do
not depend on sign of charge
 Replace q by /q/

## Slide 4: Resistivity and Resistance
Properties of material matter too:
For metals, at T = const. J= nqvd ~ E
Proportionality constant r is resistivity r = E/J Ohm’s law
Reciprocal of r is conductivity
Unit r: [Wm] ‘Ohm’ = [(V/m) / (A/m2)] = [Vm/A]

## Slide 5
Types of resistivity

## Slide 6
Ask for total current in and
potential at ends of conductor:
Relate value of current to
Potential difference between ends.
For uniform J,E
I = JA and V =EL
with Ohm’s law E=rJ
V/L = rI/A
Const. r  I ~ V
‘resistance’ R = V/I [W]
vs. R
R =rL/A
R = V/I
V = R I
I = V/R
Resistance

## Slide 7
Electromotive Force
Steady currents require circuits: closed loops of conducting material
otherwise current dies down after short time
Charges which do a full loop
must have unchanged potential
energy
Resistance always reduces U
A part of circuit is needed which
increases U again
This is done by the emf.
Note that it is NOT a force but
a potential!
First, we consider ideal sources (emf) : Vab = E = IR

## Slide 8
I is not used up while flowing from + to –
I is the same everywhere in the circuit
Emf can be battery (chemical), photovoltaic (sun energy/chemical),
from other circuit (electrical), every unit which can create em energy
EMF sources usually possess Internal Resistance. Then,
Vab = E – Ir and I = E/(R+r)

## Slide 9: Resistor networks
Careful: opposite to capacitor series/parallel rules!

## Slide 10
Circuit Diagrams
I = E/(R+r) = 2A
Va’b’= Vab = IR = E-Ir = 8V
(Ideal wires and am-meters have
Zero resistance)
No I through voltmeter
(infinite R) …
i.e. no current at all
Va’b’ = IR = 0 = Vaa’
Vbb’ = Vab
Voltage is always measured in parallel, amps in series

## Slide 11: Energy and Power in Circuits
Rate of conversion to electric energy: EI, rate of dissipation I2r –
difference = power output source
When 2 sources are connected to simple loop:
Larger emf delivers to smaller emf

## Slide 12: Combining Measuring Instruments

## Slide 13
Group Task:
Find Req and I and V across
/through each resistor!

## Slide 14
Group task:
Find I25 and I20

## Slide 15
Kirchhoff’s Rules
A more general approach to analyze resistor networks
Is to look at them as loops and junctions:
This method works even
when our rules to reduce
a circuit to its Req
fails.

## Slide 16
‘Charging a battery’
Circuit with more
than one loop!
Apply both rules.
Junction rule,
point a:
-I + 1A + 2A =0
I = 3A
[Similarly point b:
I – 1A – 2A = 0]
Loop rule: 3 loops
to choose from
‘1’: decide direction
in loop – clockwise
(sets signs!)
12V – 3A r
– 2A 3W = 0
r = 2W
Find E from loop 2:
Lets do the loop counterclockwise: E -1A1W +2A3W =0  E = -5V

## Slide 17
5 currents
Use junction rule
at a, b and c
3 unknown currents
Need 3 eqn
Loop rule to 3 loops:
cad-source
cbd-source
cab
(3 bec.of no.unknowns)
13V -I1R1-(I1-I3)R4 =0
-I2R2-(I2+I3)R5+13V=0
-I1R1-I3R3+I2R2 =0
Let’s set R1=R3=R4=1W
And R2=R5=2W
Solve for one I and
substitute in other eqn
(use easiest)
I2= ½ (I1+I3)
Group task: Find values of I1,I2,and I3!
I1 = 6.5A, I2 = 3.25A, I3 = 0

## Slide 18
Capacitance
E ~ /Q/  Vab ~ /Q/
Double Q:
Charge density, E, Vab
double too
But ratio Q/Vab is constant
Capacitance is measure of ability of a capacitor to store energy!
(because higher C = higher Q per Vab = higher energy
Value of C depends on geometry (distance plates, size plates, and material
property of plate material)

## Slide 19
Plate Capacitors
E = s/e0
= Q/Ae0
For uniform field E and given plate distance d
Vab = E d
= 1/e0 (Qd)/A
Units: [F] = [C2/Nm] = [C2/J] … typically micro or nano Farad

## Slide 20: Capacitor Networks
In a series connection, the magnitude of charge on all plates is the same. The potential differences are not the same.
Vac = Q/C1, Vcb = Q/C2 Vab = Q (1/C1 + 1/C2)
Or using concept of equivalent capacitance
1/Ceq = 1/C1 + 1/C2 + …
In a parallel connection, the potential difference for all individual capacitors is the same. The charges are not the same.
Q1 = C1 V, Q2 = C2 V Q = (C1 + C2) V
Or Ceq = C1 + C2 + …

## Slide 21
Equivalent capacitance is used to simplify networks.
Group task: What is the equivalent capacitance
of the circuit below?
Step 1:
Find equivalent for C series at right
Hand. 1/C = 1/12 + 1/6 [mF]
Step 2:
Find equivalent for C parallel
left to right.
C = 3 + 11 + 4 [mF]
Step 3:
Find equivalent for series.
C = 1/18 + 1/9 [mF]
= 6 mF
Solution: parallel branch … 10+5= 15
series branch … 1/20 + 1/10 = 1/C
 C = 20/3
 total: 2 branches in series 1/15 + 3/20
Ctot = 60/(4+9)

## Slide 22
Capacitor Networks
24.63
C1 = 6.9 mF, C2= 4.6mF
Reducing the furthest right leg
(branch):
C=(1/6.9 + 1/6.9 + 1/6.9)-1 = 2.3mF
Combines parallel with nearest C2:
C = C1eq+C2 = 6.9mF
Leaving a situation identical to what we have just worked out:
1/6.9 + 1/6.9 + 1/6.9 = 2.3 mF
And again 2.3+4.6 = Ceq,2 = 6.9 mF
So the overall CEQ = 2.3 mF
Charge on C1 and C2:
QC1 = CEQV, for V=420V 0.97 mC
QC2 = C2V2 = 4.6mF * 420/3 = 0.644 mC
For Vab = 420[V], Vcd=?
Vac = Vbd = 1/3 (420[V]), Vcd= 1/3 (1/3 420[V]))

## Slide 23: Energy Storage in Capacitors
V = Q/C
W = 1/C int0Q [q dq] = Q2/2C

## Slide 24
Energy Storage in Capacitors
24.24: plate C 920 pF, charge on each plate 2.55 mC
V between plates:
V = Q/C = 2.55 10-6C/0.920 10-9F
= 2.772 kV
b)For constant charge, if d is doubled, what will V be?
If q is constant, C must be halved and V doubled: 5.544 kV
c) How much work to double d?
U = ½ C V2 = 3.53 mJ
If d is doubled, C  ½ C  U doubles
Work equals amount of extra energy needed which is 3.53 mJ

## Slide 25: Other common geometries
Spherical capacitor
Need Vab for C, need E for Vab:
Take Gaussian surface as sphere
and find enclosed charge
E dA = E 4pr2 = Q/e0  E
Va – Vb = Q/4pe0ra- Q/4pe0rb
= q/4pe0 [(rb-ra)/rarb]
C = Q/Vab = 4pe0 rarb/(rb-ra)
Note: independent of Q and V
again.
Cylindrical capacitor
Find E Er = l/2pe0 1/r
Find V Vab = l/2pe0 lnrb/ra
Find C Q = lL, C = 2pe0L/ ln(rb/ra)
What is C dep. On?

## Slide 26
Dielectrics
Dielectric constant K
K= C/C0
For constant charge:
Q=C0V0=CV
And V = V0/K
Dielectrics are never
perfect insulators: material
leaks

## Slide 27
Induced charge: Polarization
If V changes with K, E must decrease too: E = E0/K
This can be visually understood considering that materials
are made up of atoms and molecules:

## Slide 28
Induced charge: Polarization – Molecular View
Dielectric breakdown

## Slide 29
Change with dielectric:
E0 = s/e0  E = (s-si)/e0 and = E0/K
s-si = e0E0/K  si = s -s/K
si = s (1-1/K)
E = s/e
Empty space: K=1, e=e0

## Slide 30
RC Circuits
Charging a capacitor
From now on
instantaneous
Quantities I and V
in small fonts
vab = i R
vbc = q/C
Kirchhoff:
E – iR –q/C = 0
i = E/R – q/RC
As q increases
towards Qf,
i decreases  0
Separate variables:
Integrate, take exp.:

## Slide 31
Discharging a capacitor
Characteristic time constant t = RC !

## Slide 32
Ex 26.37 - C= 455 [pF] charged with 65.5 [nC] per plate
C then connected to ‘V’ with R= 1.28 [MW]
iinitial?
b) What is the time constant of RC?
i = q/(RC) = 6.55 10-8 [C] / (1.28 106 [W] 4.55 10-10[F])
= 1.12 10-4[A]
[C/(WF] =! [A]
b) t = RC = 1.28 106 [W] 4.55 10-10 [F] = 0.582 [ms]
Group Task:
Find t
charged fully after 1[hr]? Y/N

## Slide 33
Ex 26.82 C= 2.36 [mF] uncharged, then connected in series to
R= 4.26 [W] and E=120 [V], r=0
Rate at which energy is dissipated at R
b) Rate at which energy is stored in C increases
c) Power output source
a) PR = V2/R = (120[V])2 = 3.38 [kW]
b) PC= dU/dt = 1/(2C) d(q2)/dt = iq/C = 0
c) Pt = E I = 120[V] (120[V]/4.26[W]) = 3.38 [kW]
d) What is the answer to the questions after ‘a long time’?
 all zero
Initially all the power output of the source is dissipated in the resistor.
After a long time energy is stored in the capacitor but the amount stored
isn't changing.
Group Task